| Environmental Protection Agency Region VIII |
| --- |
| 1595 Wynkoop Street (8P-W-DW) |
| Denver, Colorado 80202-2466 |
| 2016 Assessment of Ground Water Under the Direct Influence of Surface Water (GWUDISW) |
| (ONLY the first page is to be completed by surveyor; |
| FILL OUT unless this source is fully treated in a surface water treatment plant) |
| Public Water System Name: |  | PWS#: |  |
| Well/Spring/Infiltration Gallery Name: |  | County: |  |
| State Engineer’s Office Ground Water Permit #: |  |  |
| Department of Environmental Quality Construction Permit #: |  |  |  |
| Date of Assessment: |  | Field Assessor: |  |
|  |  | Index Points | Score* |
| A | TYPE OF SUBSURFACE WATER SOURCE (Highlight or Circle One) |  |  |  |  |
|  | Spring |  | 10 |  |  |
|  | Infiltration Gallery more than 2 ft. deep |  | 10 |  |  |
|  | Infiltration Gallery at or less than 2 ft. deep |  | 25 |  |  |
| B | HYDROGEOLOGICAL FEATURES (Highlight or Circle) |  |  |  |  |
|  | Surface runoff drains toward well, spring or infiltration gallery |  | 15 |  |  |
| C | STRUCTURAL FEATURES (Highlight or Circle) |  |  |  |  |
|  | WELLS (includes wells collecting water from infiltration galleries) |  |  |  |  |
|  | Uncased or Unsealed (lacking annular seal) Well |  | 40 |  |  |
|  | Lack of watertight sanitary seal on well cap (including lack of watertight bolt holes, watertight pump support openings, watertight electrical cable openings, etc.) |  | 15 |  |  |
|  | Well height not properly terminated (well, including the pitless adapter units, does not terminate a minimum of 18 inches above the final ground level, 12 inches above the pump house floor or 3 feet above the highest known flood elevation, whichever is higher. Measurements should be taken from the pump house floor, not the bottom of a pit which may be located within the pump house) |  | 15 |  |  |
|  | SPRING COLLECTION BOX (includes collection vaults collecting water from infiltration galleries) |  |
|  | Deep-rooted vegetation (e.g. trees, shrubs) around spring box, providing conduit for surface water into spring water |  | 15 |  |  |
|  | Spring box is not watertight, with overlapping lid or cover |  | 15 |  |  |
|  | Overflows or drains open to atmosphere or allow entrance of animals (unscreened) |  | 15 |  |  |
|  | Marshy (standing water) around spring collection area |  | 30 |  |  |

| GWUDISW Assessment, Continued (p. 2) |
| --- |
| (Second page to be completed by EPA Region VIII) |
| PWSID #: |  | Date: |  | EPA Assessor: |  |
|  |  | Index Points | Score* |
| A | TYPE OF SUBSURFACE WATER SOURCE (Highlight or Circle one) |  |  |  |  |
|  | Well, with depth to first screen or perforation equal to or greater than 50 feet |  | 0 |  |  |
|  | Well, with depth to first screen or perforation equal to or less than 50 feet |  | 5 |  |  |
| B | HISTORICAL MICROBIOLOGICAL CONTAMINATION (Highlight or Circle) |  |  |  |  |
|  | History or suspected outbreak of Giardia or other pathogenic organisms associated with surface water with current system configuration |  | 50 |  |  |
|  | Record of Total Coliform (TC+) acute MCL violations over the last 3 years (these violations will be reported as “MCL (TCR), ACUTE) |  | 30 |  |  |
|  | Ground Water Rule triggered Source sample(s) over the last 3 years. |  |  |  |  |
|  | TC+ in source water: | 1 TC+ |  | 20 |  |  |
|  |  | 2 TC+ |  | 25 |  |  |
|  |  | 3 TC+ |  | 30 |  |  |
|  | e. Coli+ in source water |  | 40 |  |  |
|  | Regulatory agency verifies complaints about turbidity or suspected waterborne disease | 10 |  |  |
| C | HYDROGEOLOGICAL FEATURES (Highlight or Circle) |  |  |  |  |
|  | Distance between a surface water source and the groundwater collector (vertical well, spring box or infiltration gallery) |  |  |  |  |
|  |  | Over 200 ft. |  | 0 |  |  |
|  |  | 100 – 200 ft. |  | 5 |  |  |
|  |  | Less than 100 ft. |  | 10 |  |  |
|  | Well, spring or infiltration gallery located on floodplain at approximate altitude of stream | 20 |  |  |
|  | Source aquifer that is unconsolidated, cavernous, or fractured |  | 15 |  |  |
|  | TOTAL SCORE (**) |  |
|  | (*) assign appropriate points even if the issue is not identified as a significant deficiency in the survey report |
|  | (**) total score of greater than or equal to 40 indicates further assessment is needed |
| COMMENTS: |